## Slide 1: Flexible-FEC
IETF 92, Dallas
25.03.2015
Mo Zanaty
Varun Singh
Ali Begen
draft-ietf-payload-flexible-fec-scheme-00

## Slide 2: Status
  Submitted -00 WG draft after honolulu
  Reviews: Thanks Magnus Westerlund

## Slide 3: Open Issue 1
Associating repair stream with source RTP Stream.
Dynamic Association in RTP
  (details next few slides)
no association in SDP
Example:
  a = rtpmap:96 VP8/90000
  a = rtpmap:98 FLEXFEC/90000
  a = fmtp:98 code=xor; repair-window=200ms

## Slide 4: Which RTP Stream(s) does the FEC refer to?
Media Source A
Media Source B
Source RTP Stream A1
Source RTP Stream A2
Source RTP Stream B1
Source RTP Stream B2
FEC RTP Stream XN
?
FEC RTP Stream YM
Thanks Peter Thatcher 
Open Issue 1

## Slide 5: Option 1: Refer by SSRC
Media Source A
Media Source B
Source RTP Stream 234398737
Source RTP Stream
234398738
Source RTP Stream
234398739
Source RTP Stream
234398740
FEC RTP Stream for 234398738
Problem: Must signal the protected SSRCs in RTP
FEC RTP Stream for 234398740
(Assuming one RTP session)
Open Issue 1

## Slide 6: Option 2: Use MID
Media Source A
Media Source B
Source RTP Stream A1
Source RTP Stream A2
Source RTP Stream B1
Source RTP Stream B2
FEC RTP Stream for MID A
?
Problem: Does not work for multiple source RTP streams per media source.
FEC RTP Stream for MID B
?
(Assuming one RTP session)
Open Issue 1

## Slide 7: Option 3: Use MID+RSID
Media Source A
Media Source B
Source RTP Stream A1
Source RTP Stream A2
Source RTP Stream B1
Source RTP Stream B2
FEC RTP Stream for MID A, RSID 2
Solution: RSID identifies the Source RTP Stream
FEC RTP Stream for MID B, RSID 2
(Assuming one RTP session)
Open Issue 1

## Slide 8: Option 3b: Use RSID alone
Media Source A
Media Source B
Source RTP Stream A1
Source RTP Stream A2
Source RTP Stream B3
Source RTP Stream B4
FEC RTP Stream for RSID A2
Solution: RSID identifies the Source RTP Stream
FEC RTP Stream for RSID B4
(Assuming one RTP session)
Open Issue 1

## Slide 9: Use of Header Extension
Source Stream 1
FEC Stream for 1
Source Stream 2
FEC Stream for 2
RSID=1
RSID=1
RSID=1
RSID=1
RSID=1
RSID=2
RSID=2
RSID=2

## Slide 10: Open issues 2
M and N occur in the RTP header for row length and column depth (non-bitmask case)
N = 0 and N = 1 currently means row FEC
Proposal:
  N = 0 indicates row FEC not followed by column FEC.
  N = 1 indicates row FEC followed by column FEC.

## Slide 11: Open issues 3
Type of protection (ToP) in SDP
  0=interleaved,
  1=non-interleaved,
  2= both
  We can do these dynamically in RTP
  keep it or remove it from SDP?
L and D in SDP
  Length and depth for fixed 2-D protection
  Only necessary for > 256 x 256.
  keep it or remove it from SDP?

## Slide 12: Next Steps
More reviews appreciated

## Slide 13: Extra Slide: M and N values
M>0, N=0  row of M non-interleaved packets starting from SN_base:
  SN, SN+1, SN+2,…, SN+(M-1)
M>0, N>0  column of N packets interleaved by every M packets starting from SN_base:
  SN, SN+(1xM), SN+(2xM),…, SN+(N-1)xM